## Slide 1: AEBN SERIES 1: Dangerous Goods, Hazardous Substances and GHS Workshop Webinar 4 April 2023 Presented by Australian Environment Business Network (AEBN) www.aebn.com.au

## Slide 2: Webinar Housekeeping – please read!
As this is a webinar we ask all participants to please note the following:
MOBILE PHONES are to be either switched off or switched to silent
SPEAKER VIEW: if you could please switch your screen to SPEAKER VIEW. To do this, take your mouse and hover over your screen and to the top RIGHT corner of your screen please click SPEAKER VIEW.
MORNING TEA: Morning Tea will be at 11.30am for 20 min
The Webinar will conclude at 1.30pm and will follow with Q&A for 15 minutes for those participants that have further queries of our presenter
QUESTIONS: This is an interactive Webinar and you are encouraged to please ask any questions that you may have of our presenter, Ross. To ask a Question, please hover over your screen with your mouse and click on the UNMUTE button. Once you have asked your question, please click MUTE – to avoid any background noise from entering the Webinar. You may also hold down your space bar to ask your question and release it after you have asked your question. Ross and the AEBN team will be here to assist you.
THANK YOU!

## Slide 3
Zoom Tips!
Double click your screen for Full Screen Mode.
When in Full Screen Mode, hover over the top of the participants bar to change your view of other participants.
To Ask Questions: When on mute, hold down the SPACE BAR to temporarily unmute yourself.
Look at the bar at the bottom of your screen for additional options.
Full screen mode
Recommended speaker view

## Slide 4: Ross Macfarlane National Chemicals Specialist Australian Environment Business Network (AEBN) Ross has over 35 years experience in chemical safety – specifically in dangerous goods and hazardous substances. Ross’ specialty is in risk management, in particular, in occupational health and safety, environmental and quality management (OHSEQ). His experience covers such industries as chemical and petrochemical, mining and metals, automotive, manufacturing, timber, pulp and paper, construction, aviation, local government, roads, and the health sectors. www.aebn.com.au

## Slide 5: Agenda
Hazardous substances and dangerous goods
  Legal compliance framework
Safety Data Sheets
Hazardous Substances
  Approved Criteria vs. GHS
  Globally Harmonised System
  GHS Labelling
Dangerous Goods
  Terminology
  Classes
  Packaging
Storage and Handling
Road and Rail Transport
Notes: 5

## Slide 6
To be able to identify and be aware of the hazards of Dangerous Goods
To make the Storage and Handling of Dangerous Goods safer
Understand the Regulations and the Dangerous Goods terminology
Your responsibilities
Packaging and Labeling
Segregation
Objectives
Notes: 6

## Slide 7: Why it matters?

## Slide 8: Australia has separate Legislation covering
Dangerous Goods
Hazardous Substances
Hazardous Chemicals
Scheduled Poisons
Security Sensitive Chemicals
Pharmaceuticals
Agricultural Chemicals
Today’s focus
Notes: 8

## Slide 9: Dangerous Goods vs. Hazardous Substances vs. Hazardous Chemicals
The term “Dangerous Goods” applies to chemicals which present immediate hazards during transport, and in Victoria and Western Australia, during storage and handling.
  In other States, “Dangerous Goods” in storage and handling are technically known as “Schedule 11 Hazardous Chemicals”
  In New Zealand, DG storage and handling falls under Hazardous Substances regulations
“Hazardous Substances” are classified under GHS based on a wider range of hazards, including harm to people during short and long-term exposure, and harm to the environment.
  In states other than VIC, these are called “Hazardous Chemicals” in the workplace.
Notes: 9
Example of a dangerous good.
Flammable Liquid
Explain what a flash point is and its impact on how dangerous a chemical will be
All dangerous goods have a un number. If they do not then they are not a dangerous good.

## Slide 10: Dangerous Goods vs. Hazardous Substances vs. Hazardous Chemicals (Cont…)
It is confusing!
In this workshop, I will mainly use Victorian terminology, i.e.
  Dangerous Goods – as classified under the Australian Code for the Transport of Dangerous Goods by Road & Rail (ADG Code), whether in the workplace or during transport
  Hazardous Substances – as classified under the Globally Harmonized System for the Classification and Labelling of Chemicals (GHS)
Notes: 10
Example of a dangerous good.
Flammable Liquid
Explain what a flash point is and its impact on how dangerous a chemical will be
All dangerous goods have a un number. If they do not then they are not a dangerous good.

## Slide 11: Hazardous Substances that are Dangerous Goods

## Slide 12: Hazardous Substances that are not Dangerous Goods

## Slide 13: Dangerous Goods
Substances which constitute a hazard from explosion, fire, toxicity, corrosivity or radioactivity
and
Which are identified by Class Labels
and
Have a UN Number
Notes: 13

## Slide 14: What are Dangerous Goods?
Substances which can pose a threat to
  Persons
  Property
  The environment
From
  Explosion
  Fire
  Poisoning
  Corrosion
  In most cases they pose a short-term risk
Notes: 14

## Slide 15: What are Hazardous Substances?
Physical hazards
    Explosion
    Fire
    Poisoning
    Radioactivity
    Corrosion
Environmental hazards
    To aquatic life
    To terrestrial vertebrates
    Ozone depleting
Health hazards
    Very toxic
    Toxic
    Harmful
    Corrosive
    Irritant
    Carcinogenic – cause cancer
    Mutagenic – cell mutation
    Sensitising – allergic reactions
    Teratogenic – birth defects
Can pose both short and long-term risks:
Notes: 15

## Slide 16: White King bleach
Dilute sodium hypochlorite (“pool chlorine”)
  Is not a Dangerous Good
Can cause eye damage and skin irritation
  Is a Hazardous Substance
Notes: 16

## Slide 17: Diesel fuel
Has a high flashpoint – will not ignite easily
  Is not a Dangerous Good
Can cause dermatitis and will irritate the eyes
  Is a Hazardous Substance
Notes: 17

## Slide 18: Rexona deodorant
  Flammable Gas of Class 2.1, UN 1950 (Aerosol)
  Is a Dangerous Good
  Is a Hazardous Substance (Physical hazard only)
Notes: 18

## Slide 19: Benzene
Flammable Liquid of Class 3
  Is a Dangerous Good
Proven Carcinogenic Material
  Is a Hazardous Substance
Notes: 19

## Slide 20: Regulatory framework

## Slide 21: Hazardous Substances
Hazardous Chemicals regulated in nationally harmonised Work Health & Safety (WHS) laws:
  ACT, NSW, NT, QLD, TAS, SA, WA, Commonwealth
  In VIC, Hazardous Substances are regulated under existing OHS Regulations
  WA adopted WHS laws in 2022, but Dangerous Goods remain outside
National review of WHS laws in 2019
GHS edition 7 mandatory as of 1-Jan-2023, replacing edition 3

## Slide 22: Storage & Handling of Dangerous Goods
In ACT, NSW, NT, QLD, SA and TAS storage and handling of Dangerous Goods is covered by WHS Regulations
  Referred to as “Schedule 11 Hazardous Chemicals”
In VIC and WA this is covered in Dangerous Goods legislation
  WA adopted harmonised WHS legislation on 31 March 2022, but maintains separate dangerous goods legislation, subject to review in 2 years
Notes: 22

## Slide 23: Dangerous Goods Transport
Not covered by the Work Health & Safety (WHS) regulations for hazardous chemicals.
These continue to be covered by state-based transport laws and the Australian Dangerous Goods (ADG) Code.

## Slide 24: Australian Code for the Transport of Dangerous Goods by Road & Rail (ADG Code)
Issued by National Transport Commission (NTC)
  Reviewed 2-yearly
ADG7.7
  Adopted 1 October 2020, mandatory 1 October 2021
  Derived from UN Recommendations on the Transport of Dangerous Goods 21st Edition (UN21)
  ADG 7.8 adopted 1/4/23.
  Mandatory 1/4/2024.
  Derived from UN22.
Model Act For The Transport of Dangerous Goods by Road and Rail 2007
  Model Subordinate Law for the Transport of Dangerous Goods By Road And Rail
Other codes
  IMDG Code (sea transport)
  IATA Regulations (air transport)

## Slide 26: Hazardous Substances
Approved Criteria for Classifying Hazardous Substances [NOHSC: 1008 (2004)]
  NOHSC – National OHS Commission – now Safe Work Australia
WA was the last jurisdiction to discontinue use, on 31/3/2023
Work Health & Safety legislation
  National Code of Practice
  Globally Harmonised System of Classification and Labelling of Chemicals (GHS, Edn. 3) mandatory from 1/1/2017
  GHS Edition 7 adopted 1/1/2021 with 2-year transition, mandatory as of 1/1/2023

## Slide 28: Regulation – Victoria
Dangerous Goods
Dangerous Goods Act 1985
  Dangerous Goods (Storage & Handling) Regulations 2022
    Code of practice for the storage and handling of dangerous goods 2013
  Dangerous Goods (Road & Rail Transport) Regulations 2018
Hazardous Substances
Occupational Health & Safety Act 2004
  Occupational Health & Safety Regulations 2017 PART 4.1—HAZARDOUS SUBSTANCES
    Compliance code: Hazardous substances

## Slide 29: Regulation – NSW
Dangerous Goods
Dangerous Goods (Road and Rail Transport) Act 2008 (NSW)
  Dangerous Goods (Road and Rail Transport) Regulation 2014
Storage & handling EXCLUDED
Hazardous Substances
Work Health and Safety Act 2011 (NSW)
  Work Health and Safety Regulation 2017 Part 7.1 Hazardous chemicals
  Division 3 Subdivision 2 Manifest of Schedule 11 hazardous chemicals (equivalent to Dangerous Goods storage & handling)
National Codes of Practice
  Managing Risks of Hazardous Chemicals in the Workplace
  Labelling of Workplace Hazardous Chemicals
  Preparation of Safety Data Sheets for Hazardous Chemicals

## Slide 30: Regulation – WA
Dangerous Goods
Dangerous Goods Safety Act 2004
  Dangerous Goods Safety (General) Regulations 2007
  Dangerous Goods Safety (Storage and Handling of Non-explosives) Regulations 2007
    Guide – Dangerous Goods Safety (Storage and Handling of Non-explosives)
  Dangerous Goods Safety (Road and Rail Transport of Non-explosives) Regulations 2007
Hazardous Substances
Work Health and Safety Act 2020 (WA)
  Work Health and Safety (General) Regulations 2022 Part 7.1 Hazardous chemicals
    Approved code of practice – Managing risks of hazardous chemicals in the workplace

## Slide 31: Regulation – New Zealand
In NZ Dangerous Goods transport is covered by the Land Transport Rule: Dangerous Goods 2005
  Administered by NZ Transport Agency
Requirements are set out in New Zealand Standard NZS 5433:2020, Transport of dangerous goods on land
  SNZ HB 5433:2021UN dangerous goods list (published 28/01/22)
Storage and handling of Hazardous Substances, including Dangerous Goods, is covered by Health and Safety at Work (Hazardous Substances) Regulations 2017
  Administered by WorkSafe New Zealand
Classification is based on Hazardous Substances & New Organisms (HSNO) Regs
NZ adopted GHS 7 from 30 April 2021, with a 4-year transition period

## Slide 32: National Legislation Cross-Reference

## Slide 33: Hazardous Substances

## Slide 34: Classification of Hazardous Substances
A substance is deemed to be hazardous if it meets criteria specified in:
Globally Harmonised System of Classification and Labelling of Chemicals 7th Revised Edition (GHS)
  Mandatory from 01/01/2023, replacing GHS 3rd Edition
  Note: UNECE now up to 9th Revised Edition (2021)
Notes: 34

## Slide 35: Globally Harmonised System of classification and labelling of chemicals (GHS)
The GHS is an internationally recognised system for the classification of chemicals
    Developed by United Nations Economic Commission for Europe (UNECE)
    Derived from existing systems, e.g. USA, Canada, EU, UN Transport of Dangerous Goods (TDG), etc.
Provides a harmonised system of hazard communication through labels and safety data sheets
Notes: 35

## Slide 36: GHS classifies chemicals according to:
Physical hazards
  9 classes, aligned to the dangerous goods classes
  Environmental hazards
  Acute aquatic toxicity
  Chronic aquatic toxicity
  Health hazards
  Acute toxicity
  Skin corrosion
  Skin irritation
Health hazards (cont.)
  Serious eye damage
  Eye irritation
  Respiratory sensitizer
  Skin sensitizer
  Germ cell mutagenicity
  Carcinogenicity
  Reproductive toxicity
  Specific target organ toxicity (STOT)
  Aspiration hazard

## Slide 37: Identifying hazards of chemicals
Section 2 of the SDS
Identifies hazardous substance chemical by:
  Pictograms (similar to DG diamonds)
  Signal Word – “WARNING” or “DANGER”
  Hazard and Precaution statements
    (Replaced Risk and Safety Phrases)
Notes: 37

## Slide 38
The GHS prescribes 9 pictograms to convey the hazards of chemicals
GHS Pictograms
Two new symbols introduced
All relevant pictograms appear on label (according to the prioritisation rules).
  In practice more than 4 pictograms is very rare
Notes: The pictograms are the same shape as the Dangerous Goods labels (a square set at a point) and most, except the exclamation mark and the “health hazard symbol”, will be familiar. These are new symbols under the GHS to help convey health hazards that were not covered by the Dangerous Goods Code.
The border is red on a white background. If the product is for the domestic market only and is not for export, then the border can be black.
Each pictogram has an official name. The “health hazard” pictogram is colloquially known as “Star Man”, “Exploding torso” and others.
Priority rules: Rules for prioritising pictograms to preserve space on label and to prevent possible contradiction of information.
If skull and crossbones appears, exclamation mark will not appear.
If corrosive appears, exclamation mark will not appear for skin or eye irritation.
If health hazard appears for respiratory sensitisation, exclamation mark will not appear for skin sensitisation or skin or eye irritation.
If a transport pictogram appears, the equivalent GHS pictogram will not appear.

## Slide 39
The GHS also allows dangerous goods class labels to be displayed on labelling and safety data sheets.
There are no equivalents to the “exclamation mark” and “health hazard” pictograms.
1
2
3
4
5
6
8
9
Dangerous Goods Class
GHS Pictograms
Notes: Manufacturers and importer can continue to use the dangerous goods diamonds on labels if they wish.
Of course, depending on transport requirements it may be mandatory to have the dangerous goods pictogram on the container.
Note there is no dangerous goods equivalent of the exclamation mark and the health hazards symbols.
Note that DG class 7 (radioactive) is not covered by GHS. Neither is 6.2 (infectious substances).

## Slide 40
GHS Pictogram for Flammable chemicals
6 different “flammable” symbols become one – intrinsic hazard not always obvious at a glance.
  Read label e.g. In contact with water releases flammable gas
  NO CHANGE TO PLACARDS - DG symbol still required
Notes: Although the workplace label may change, the placard symbol will not. Therefore, in emergency situations, fire crews and response personnel will still have the information to deal with the situation.
Manufacturers can choose to put the dangerous goods symbol on labelling.

## Slide 41: Hazard & Precaution Statements
  H followed by 3 numbers
  Physical hazards
  H225 Highly flammable liquid and vapour
  Health Hazards
  H302: Harmful if swallowed
  H350: May cause cancer
  Enviro hazards
  H410: Very toxic to aquatic life with long-lasting effects
  Country-specific (Australia)
  AUH014: Reacts violently with water
  P followed by 3 numbers
  General
    P102: Keep out of reach of children
  Prevention
    P233: Keep container tightly closed
  Response
    P372: Explosion risk in case of fire
  Storage
    P420: Store away from other materials
  Disposal
    P501: Dispose of contents/container to …

## Slide 42: Changes from GHS 3 to GHS 7 – Australia
New hazard categories and classes for:
  Non-flammable aerosols
  Chemically unstable gases
  Pyrophoric gases
  Desensitised explosives
Adoption of eye irritant category 2B
Updated precautionary statements.
See Safe Work Australia guidance:
  GHS 7 – transition (including 15-minute Youtube webinar)
  Changes to chemical classifications and labelling under GHS 7

## Slide 43: Changes from HSNO to GHS 7 – New Zealand
From 2001 EPA NZ classified substances based on Hazardous Substances & New Organisms (HSNO) legislation which broadly aligns to DGs and GHS,
Since adoption of HSW Act 2015 and HSW (Hazardous Substances) Regs 2017, hazardous substances regulation is transitioning from EPA NZ to WorkSafe NZ
NZ adopted GHS 7 on 30 April 2021 with a 4-year transition for existing substances to comply with updated labelling, safety data sheets and packaging notices..
See : New Zealand’s hazard classification system (EPA NZ)
  HSNO to GHS7 Correlation table (PDF, 241KB)

## Slide 44: Safety Data Sheets (SDS)
A Safety Data Sheet (SDS) is a technical bulletin containing detailed information about a hazardous substance.
  Formerly known as a Material Safety Data Sheet (MSDS)
An SDS must comply with VIC OHS Regulation 145
  WHS Regulations Part 7.1 Division 2
  NZ HSW (Hazardous Substances) Regulation 2.11
The hazard identification for the substance must be determined in accordance with the GHS.

## Slide 45: Safety Data Sheet (Cont.)
Is an advisory document
Provides information on particular substances
However, producer of document picks up responsibility for:
  Completeness
  Accuracy
Duty of care

## Slide 46: Safety Data Sheet (Cont.)
The manufacturer or importing supplier of a hazardous substance must ensure an SDS is prepared
Manufacturer or supplier must ensure a copy is provided
  on or before the first occasion that the substance is supplied to a person,
  after the SDS is reviewed
  to any employer who intends to use that hazardous substance in a workplace, on request.

## Slide 47: Should a Safety Data Sheet be less than 5 years old?
YES!
VIC OHS Reg 146 Review and revision of safety data sheet
  A manufacturer or an importing supplier of a hazardous substance must ensure that the safety data sheet for a substance is reviewed—
  as often as is necessary to ensure that the safety data sheet contains current and accurate information; and
  at least every 5 years.
  AND
An employer must ensure that a current safety data sheet is available (Reg 155 and 156).
WHS Reg 330:
  (3) The manufacturer or importer of the hazardous chemical must:
  (a) review the safety data sheet at least once every 5 years…

## Slide 48: 16 Header SDS – Sections
Section 1 Identification of the material and supplier
Section 2 Hazards identification
Section 3 Composition/information on ingredients
Section 4 First aid measures
Section 5 Fire fighting measures

## Slide 49: 16 Header SDS – Sections (Cont.)
Section 6 Accidental release measures
Section 7 Handling and Storage
Section 8 Exposure Control / Personal Protection
Section 9 Physical and chemical properties
Section 10 Stability and reactivity

## Slide 50: 16 Header SDS – Sections (Cont.)
Section 11 Toxicological information
Section 12 Ecological information
Section 13 Disposal considerations
Section 14 Transport information
Section 15 Regulatory information
Section 16 Other information

## Slide 52: Safety Data Sheet Exercise
What is the issue date of the SDS?
What is the Product Name and name of the supplier?
  Section 1
Is the material Hazardous? If yes, write down one (1) Hazard Statement.
  Section 2
Is it a Dangerous Good? If so, what is the UN Number and Proper Shipping Name?
  Section 14
Which section describes physical and chemical properties of the material? Write down two (2) of its physical or chemical properties.

## Slide 53
What is the issue date of the SDS?
What is the Product Name and name of the supplier?
  Section 1

## Slide 54
Is the material Hazardous? If yes, write down one (1) Hazard Statement.
  Section 2

## Slide 55
Is it a Dangerous Good? If so, what is the UN Number and Proper Shipping Name.
  Section 14

## Slide 56
Which section describes physical and chemical properties of the material? Write down two (2) of its physical or chemical properties.

## Slide 57: Safety Data Sheet Exercise
What is the issue date of the SDS?
  26 June 2019
What is the Product Name and name of the supplier?
  Redox Sodium Nitrate
Is the material Hazardous? If yes, write down one (1) Hazard Statement.
  Yes: H272 May intensify fire; oxidizer, H319 Causes serious eye irritation.

## Slide 58: Safety Data Sheet Exercise
Is it a Dangerous Good? If so, what is the UN Number and Proper Shipping Name?
  UN Number 1498, Proper Shipping Name SODIUM NITRATE
Which section describes physical and chemical properties of the material? Write down two (2) of its physical or chemical properties.
  Physical State Solid, Appearance Crystalline (powder), Odour Odourless, Colour White, etc.

## Slide 59: Hazardous Substances Register
Legal requirement
  VIC OHS Reg 162 and DG (S&H) Reg 58
  WHS Regulation 346
List of product names of all Hazardous Substances in the workplace, including Dangerous Goods and combustible liquids
Accompanied by the current SDS
Can (should!) be combined with Dangerous Goods Register

## Slide 60: DG & Hazardous Substance Register
Supplier | Product | Issue Date | Expiry Date | Eye Hazard | Skin Hazard | Inhalation | Ingestion | DG Class
BOC Gases | Argoshield Light | 19/08/2021 | 19/08/2026 | No | No | No | No | 2.2 Non-Flammable Non-Toxic Gas
BOC Gases | Oxygen, Compressed | 19/08/2021 | 19/08/2026 | No | No | No | No | 2.2 Non-Flammable Non-Toxic Gas
bp | Automotive Diesel Fuel | 8/06/2019 | 7/06/2024 | Yes | Yes | Yes | Yes | Combustible Liquid
bp | Regular Unleaded Petrol | 26/05/2021 | 26/05/2026 | Yes | Yes | Yes | Yes | 3 Flammable Liquid
Castrol | Activ 2T | 15/12/2022 | 15/12/2027 | No | No | No | No | Combustible Liquid
Castrol | GTX 20W-5 | 10/03/2023 | 9/03/2028 | No | No | No | No | No
Castrol | Hyspin AWS 68 | 3/03/2023 | 2/03/2028 | No | No | No | No | No
Castrol | Spheerol EPL 2 Grease | 21/01/2021 | 21/01/2026 | No | No | No | No | No

## Slide 61: Dangerous Goods

## Slide 62: Recap: Hazardous Substances vs. Dangerous Goods
Dangerous goods are classified based on immediate hazards during transport, storage and handling, e.g. explosion, fire, toxicity, corrosivity and radioactivity
Hazardous substances are classified based on the risks they pose to people during short and long-term exposure
While the categories overlap, they are not the same
The categories are not static – they are changing progressively, in Australia and internationally
Notes: 62
Example of a dangerous good.
Flammable Liquid
Explain what a flash point is and its impact on how dangerous a chemical will be
All dangerous goods have a un number. If they do not then they are not a dangerous good.

## Slide 63: ADG Code
Australian Code for the Transport of Dangerous Goods by Road & Rail (ADG Code)
Maintained by the National Transport Commission (NTC).
Mainly intended for transport, but applies to manufacture and storage in relation to classification, labelling and packaging.

## Slide 64: ADG Code (Cont…)
ADG7 replaced ADG6 in 2007, to align line with the UN Recommendations on the Transport of Dangerous Goods, 13th Edition (UN13).
Current version: ADG7.7, based on UN21, adopted 1 October 2020; mandatory as of 1 October 2021
ADG Code is reviewed 2-yearly based on UN Recommendations
  Draft ADG 7.8, based on UN22, was adopted for use from 1 April 2023 and will be mandatory from 1 April 2024.

## Slide 65: Structure of the ADG Code
The Code consists of:
  13 Parts
  4 Appendices
Notes: 65

## Slide 66: Structure of the ADG Code (Cont…)
General Provisions, Definitions and Interpretation
Classification
Dangerous Goods Lists, Special Provisions and Limited Quantities Exceptions
Packing, Tank, Container, Vehicle and Equipment Provisions
Consignment Procedures – Including Labelling, Marking and Placarding
Requirements for the Construction and Testing of Packagings, IBCs, Large Packagings, Portable Tanks, MEGCs, Bulk Containers, Tank Vehicles, Freight Containers & Segregation Devices
Notes: 66

## Slide 67: Structure of the ADG Code (Cont…)
Provisions Concerning Transport Operations
Stowage and Restraint
Segregation
Bulk Transfer of Dangerous Goods
Documentation
Safety Equipment for Road Vehicles
Procedures during Road Transport
Notes: 67

## Slide 68: Structure of the ADG Code (Cont…)
Four Appendices:
Goods too dangerous to be transported
Forms
Hazchem codes
Code of practice for reprocessing steel drums
Notes: 68

## Slide 69: Classification of Dangerous Goods
CLASS
  DIVISION
SUBSIDIARY HAZARD
PACKING GROUP
UN NUMBER
PROPER SHIPPING NAME
Notes: UN number is a number designated by the UN for each chemical
This UN number can also be used where there are formulations and these form part of the groups that have NOS on the end of them
NOS meaning ..........
Proper Shipping Name is the UN designated name for the product and it is the name in the product list which is in capitals
Class has already been discussed.
Sub risk - In some cases a chemical can have one or more sub hazard as well as a major risk factor.
e.g. Draw on board.

## Slide 70: DG Class, Division & Subsidiary Hazard
CLASS means the Class of Dangerous Goods as shown in the ADG Code
Within the Classes, there are DIVISIONS
Substances can be classified within 2 or more Classes, with secondary Class(es) referred to as SUBSIDIARY HAZARDS
Notes: Show the students the class chart on the wall and explain to
them the changes in some of the class descriptions e.g. poison
Show the video on classes

## Slide 71: Class 1: Explosives
Some Explosive Articles |  |  | 
Ammunition | Flash Powder | Smokeless Powder | Sounding Devices
Black Powder | Fuse | Primer | Torpedoes
Bombs | Fuse (Ammo) | Projectiles | Warheads
Charges | Igniters | Propellants | 
Fireworks | Mines | Rocket Motors | 
Flares | Powder cake | Signals | 

## Slide 72: Division 2.1 Flammable Gases
Gases which ignite on contact with a source of ignition, however:
They only ignite in a certain range of concentrations with air
Above the upper limit – too rich to burn
Below the lower limit – too lean to burn
Heavier-than-air gas leaks may flow and accumulate in low points
  e.g. propane, butane (LPG)
Notes: 72

## Slide 73: Aerosols

## Slide 74: Division 2.2 Non-Flammable Non-Toxic Gases
Not Flammable when exposed to a source of ignition
Not Toxic, but can cause death by asphyxiation
Most are heavier than air, many 6 or 7 times heavier
Some are stored in cryogenic form, i.e. below minus 150OC
Oxygen has sub-hazard 5.1
Notes: 74

## Slide 75: Oxidising Gas
Division 2.5
This class diamond can be used for road and rail transport in Australia in place of class 2.2 and sub-hazard 5.1
It is not used internationally and cannot be used for sea freight (IMDG)
Examples:
  Oxygen gas
  Nitrous oxide

## Slide 76: Division 2.3 – Toxic Gas
Most toxic gases are heavier than air and many have a subsidiary hazard
Ammonia, Anhydrous Sub-Hazard 8
Arsine SH 2.1
Bromine Chloride SH 5.1 & 8
Chlorine SH 5.1 & 8
Notes: 76

## Slide 77: Class 3: Flammable Liquids
The UN defines a flammable liquid as:
  Any liquid having a flash point not more than 60o C
A C1 combustible liquid has a flash point above 60o C and below 93o C
Notes: 77

## Slide 78: Class 4: Flammable Solids
Class 4 includes 3 Divisions with different diamonds:
4.1 Flammable solids
4.2 Spontaneously combustible
4.3 Dangerous when wet
Notes: 78

## Slide 79: Division 4.1 Flammable Solids
Can be easily ignited by flames, sparks etc and are readily combustible
Danger may also come from toxic combustion products
Examples: sulphur
red phosphorus
  magnesium
  matches
  firelighters
Notes: 79

## Slide 80: Division 4.1 Flammable Solids
Includes
  Readily Combustible Solids
  Desensitized Explosives
  Self-Reactive Materials
    Classified into Types A, B, C, D, E, F and G
Notes: 80

## Slide 81: Division 4.2 - Spontaneously Combustible
Can burst into flames without an external source of ignition being applied
Two types:
Pyrophoric materials
Self-heating materials
Examples:
White phosphorous (kept under water)
Activated carbon
Iron swarf
Notes: 81
The UN defines a spontaneously combustible material as either of the following:
A pyrophoric material is a liquid or solid that even in small quantities and without external ignition source can ignite within five minutes after coming in contact with air.
A self-heating material is a material that when in contact with air and without an energy supply is liable to self heat.

## Slide 82: Division 4.3 - Substances which in contact with water emit flammable gases
When they react with water, these substances are liable to become spontaneously flammable due to the heat liberated by the reaction.
Examples:
sodium (gives off hydrogen)
calcium carbide (gives off acetylene)
Notes: 82

## Slide 83: Division 5.1 – Oxidizing Agents
Not necessarily combustible but can liberate oxygen and therefore increase ferocity of a fire
Examples:
Sodium Nitrate
Hydrogen Peroxide
Notes: 83

## Slide 84: Division 5.2 – Organic Peroxides
Can react with organic materials to cause fire
Example:
  Epoxy adhesive hardener, MEKP (Methyl Ethyl Ketone Peroxide)
This DG Class Diamond is no longer used (discontinued as of 2011)
Notes: 84

## Slide 85: Division 6.1 - Toxic Substances
Liable to cause death or serious injury or be harmful to health if swallowed, inhaled or by skin contact
Examples:
Sodium cyanide
N,N-dimethylaniline
Alkaloids, solid, N.O.S.
Trichlorethylene
Methylene chloride
Notes: 85
The UN defines Toxic Substance 6.1 as follows:
A toxic material is a material (other than a gas) that is known to be toxic to humans, or
Is presumed to be toxic because of data obtained from tests performed on animals, or
Is an irritating material with properties similar to tear gas and causes extreme irritation, especially within confined spaces.

## Slide 86: Division 6.2 Infectious Substances
An infectious substance is a viable microorganism or its toxin that causes or can cause disease in humans or animals.
Potentially infectious substances include:
Blood and blood products
Skin, tissue, cell cultures
Pathogens
  (viruses, bacteria, parasites, etc.)
  This placard is used for transport but is not required for storage areas.
Notes: 86

## Slide 87: Class 7: Radioactive Materials
Radioactive White-I, Yellow-II, and Yellow-III alerts emergency response workers to increasing radioactivity.
White-I is the least radioactive and Yellow-III is the most radioactive.
Notes: 87
A radioactive material is any material or any combination of materials that spontaneously emits ionizing radiation having a specific activity greater than 70 Becquerels per gram.
  Measured with a Geiger Counter.
Radioactive White-I, Yellow-II, and Yellow-III alerts emergency response workers to increasing radioactivity.
White-I is the least radioactive and Yellow-III is the most radioactive.

## Slide 88: Class 8 - Corrosives
A corrosive material is either of the following:
Liquid or solid that causes visible destruction or irreversible alterations in skin tissue at the site of contact.
Liquid that has a severe corrosion rate on steel or aluminum, as measured in accordance with certain prescribed UN testing procedures.
Examples:
Solids sodium hydroxide pellets
Liquids hydrochloric acid
Notes: 88

## Slide 89: Class 8 - Corrosives
Most corrosives are either Acidic or Alkaline
Acids – pH LESS THAN 7
  Hydrochloric
  Sulphuric
Alkalis – pH GREATER THAN 7
  Sodium hydroxide
  Potassium hydroxide
Class 8 Acids and Alkalis must be segregated
  Check pH in the SDS: SECTION 9 PHYSICAL AND CHEMICAL PROPERTIES
Notes: 89

## Slide 90: Class 9: Miscellaneous Hazardous Materials
Materials that present a hazard during transportation but not included in any other hazard class.
Examples
  materials with anesthetic or noxious properties
  elevated-temperature substances – e.g. hot bitumen
  hazardous wastes
  marine pollutants
  magnetized materials,
  lithium batteries (risk of fire if damaged)
Notes: 90

## Slide 91: Other Dangerous Goods Diamonds
Multi Class diamond – used for transport
Goods too dangerous to be transported
Environmentally Hazardous mark

## Slide 92: Subsidiary Hazard
A secondary hazard (or risk) that meets the UN criteria
e.g. Hydrogen peroxide
  Class 5.1
  Subsidiary hazard 8

## Slide 93: Packing Group
Packing Group I
  Great Danger
Packing Group II
  Medium Danger
Packing Group III
  Minor Danger
Used for packing purposes, to classify common DGs
NOT used for explosives, gases, radioactives, organic peroxides, infectious substances and some class 4 substances

## Slide 94: DG Packing Group vs. GHS Category
GHS refers to “Categories” which are aligned to DG Packing Groups
  e.g. DG Class 3 Flammable Liquids
DG PG | GHS Category | Criteria | Hazard Statement
I | 1 | Flash point < 23°C and initial boiling point ≤ 35°C | H224 Extremely flammable liquid and vapour
II | 2 | Flash point < 23°C and initial boiling point >35°C | H225 Highly flammable liquid and vapour
III | 3 | Flash point ≥ 23°C and ≤ 60°C | H226 Flammable liquid and vapour
 | 4 | Flash point > 60°C and ≤ 93°C | H227 Combustible liquid

## Slide 95: UN Number
Internationally recognized 4-digit number – mainly used in transport.
Maybe specific to a chemical, or generic to a class – e.g.
  UN 1114 BENZENE
  UN 1950 AEROSOLS
  UN 2921 CORROSIVE SOLID, FLAMMABLE, N.O.S. (Not Otherwise Specified)
  UN 3480 LITHIUM ION BATTERIES (including lithium ion polymer batteries)

## Slide 96: Proper Shipping Name
  2790 ACETIC ACID SOLUTION more than 10% but not less than 80% acid by mass
The proper shipping name is the part of the description shown in upper case

## Slide 97: Special Classifications
Materials transported at or above their flash point are classified as flammable liquids
  UN 3256 ELEVATED TEMPERATURE LIQUID, FLAMMABLE, N.O.S.
    Example is hot bitumen
Liquids transported above 100oC, and solids transported above 240oC are Class 9
  UN 3257 ELEVATED TEMPERATURE LIQUID, N.O.S.
  UN 3258 ELEVATED TEMPERATURE SOLID, N.O.S.

## Slide 98
ELEVATED TEMPERATURE
LIQUID FLAMMABLE
HAZCHEM
2Y
UN No.
3256
IN EMERGENCY, DIAL
000, POLICE OR FIRE BRIGADE
SPECIALIST ADVICE
131 700

## Slide 99: Fire Risk Dangerous Goods
Goods which burn readily or support combustion
Classes 2.1, 3, 4 or 5, or products with
a 2.1, 3, 4 or 5 sub-hazard

## Slide 100: SUSMP (Poisons Schedule) Standard for the Uniform Scheduling of Medicines and Poisons
Schedule | Description
Schedule 2. | Pharmacy Medicine
Schedule 3. | Pharmacist Only Medicine
Schedule 4. | Prescription Only Medicine, or Prescription Animal Remedy
Schedule 5. | Caution
Schedule 6. | Poison
Schedule 7. | Dangerous Poison
Schedule 8. | Controlled Drug
Schedule 9. | Prohibited Substance
Schedule 10 | Substances of such danger to health as to warrant prohibition of sale, supply and use
A Health Department Poisons License may be required to manufacture, store, supply or use certain Schedule 7 poisons

## Slide 101: Packaging
Dangerous Goods for transport must be in approved packaging.
  Prescribed packaging (e.g. Gas cylinders)
  Packaging that has a requirement to pass a testing standard (e.g. Steel drum)
Notes: ONE SHOULD ALWAYS PACK GOODS EVEN IF THEY ARE FOR STORAGE ONLY IN SAFE WELL MARKED PACKAGING.

## Slide 102: Prescribed Packaging
Particular forms of packaging are prescribed for some classes of Dangerous Goods
Class 2 Gases
Division 4.1 Self-reactive substances only
Division 5.2 Organic Peroxides

## Slide 103: Approved Package Marking

## Slide 104: Other Information
ADG includes a large amount of specific detail about packaging and transport – e.g.

## Slide 105: URL - additional information
Australian Dangerous Goods Code (ADG )
  http://www.ntc.gov.au/heavy-vehicles/safety/australian-dangerous-goods-code/
Safe Work Australia
  www.safeworkaustralia.gov.au
National Transport Commission – ADG Code
  https://www.ntc.gov.au/codes-and-guidelines/australian-dangerous-goods-code
UN Model Regulations for the Transport of Dangerous Goods
  https://unece.org/info/publications/pub/364867
Global Harmonisation System (GHS) – UNECE
  https://www.unece.org/trans/danger/publi/ghs/ghs_welcome_e.html
Labelling of Agricultural and Veterinary chemicals
  https://apvma.gov.au/registrations-and-permits/labelling-codes
Poisons Schedule (SUSMP)
  https://www.tga.gov.au/publication/poisons-standard-susmp
Notes: 105

## Slide 106: URL - additional information
EPA NZ – Hazardous substances classification
  https://www.epa.govt.nz/industry-areas/hazardous-substances/new-zealands-new-hazard-classification-system/
WorkSafe New Zealand – Hazardous Substances
  https://www.worksafe.govt.nz/topic-and-industry/hazardous-substances/
Hazardous Substances Toolbox
  https://www.hazardoussubstances.govt.nz/
NZ Land Transport Agency
  https://nzta.govt.nz/resources/rules/dangerous-goods-2005-index/
NZ Health and Safety at Work (Hazardous Substances) Regulations
  https://www.legislation.govt.nz/
Notes: 106

## Slide 107: Australian & New Zealand Standards
  AS 1940–2017 The storage and handling of flammable and combustible liquids
  AS 2243.2:2021 Safety in laboratories, Part 2: Chemical aspects and storage
  AS 3780–2008 The storage and handling of corrosive substances
  AS/NZS 3833:2007 The storage and handling of mixed classes of dangerous goods, in packages and intermediate bulk containers
  AS 4332–2004 (R2016) The storage and handling of gases in cylinders
  AS/NZS 4452:1997 The storage and handling of toxic substances
  AS/NZS 4681:2000 The storage and handling of Class 9 (miscellaneous) dangerous goods and articles
  AS/NZS 5026:2012 The storage and handling of Class 4 dangerous goods
  NZS 5433:2020 Transport of dangerous goods on land
  SNZ HB 5433:2021 UN dangerous goods list

## Slide 108: Sources of information
Physical inspection
Internal and external audits
Employee knowledge and expertise
Trade journals
WorkCover alerts and publications
Incident /injury records
Industry associations
Notes: 108

## Slide 109: Sources of information (Cont…)
Product information
Technical data sheets
Manufacturers instruction manuals
Personal contacts
By asking ‘What if?’
Brainstorming
Notes: 109

## Slide 110: AEBN SERIES 1: Dangerous Goods, Hazardous Substances and GHS Workshop Webinar 4 April 2023 Presented by Australian Environment Business Network (AEBN) National Office 100 Douglas Pde Williamstown Vic 3016 (PO Box 588 Altona Vic 3018) T +61 3 9397 2511 | E aebn@aebn.com.au www.aebn.com.au