## Slide 1: Webinar Housekeeping – please read!
As this is a webinar we ask all participants to please note the following:
MOBILE PHONES are to be either switched off or switched to silent
SPEAKER VIEW: if you could please switch your screen to SPEAKER VIEW. To do this, take your mouse and hover over your screen and to the top RIGHT corner of your screen please click SPEAKER VIEW.
MORNING TEA: Morning Tea will be at 11.30am for 20 min
The Webinar will conclude at 1.30pm and will follow with Q&A for 15 minutes for those participants that have further queries of our presenter
QUESTIONS: This is an interactive Webinar and you are encouraged to please ask any questions that you may have of our presenter, Ross. To ask a Question, please hover over your screen with your mouse and click on the UNMUTE button. Once you have asked your question, please click MUTE – to avoid any background noise from entering the Webinar. You may also hold down your space bar to ask your question and release it after you have asked your question. Ross and the AEBN team will be here to assist you.
THANK YOU!

## Slide 2: AEBN SERIES 2: Dangerous Goods and Hazardous Substances Workshop Webinar 5 April 2023 Presented by Australian Environment Business Network (AEBN) www.aebn.com.au

## Slide 3
Zoom Tips!
Double click your screen for Full Screen Mode.
When in Full Screen Mode, hover over the top of the participants bar to change your view of other participants.
To Ask Questions: When on mute, hold down the SPACE BAR to temporarily unmute yourself.
Look at the bar at the bottom of your screen for additional options.
Full screen mode
Recommended speaker view

## Slide 4: Agenda
Refresher – Intro to Dangerous Goods (DG)
Storage and Handling
Road and Rail Transport

## Slide 5: Legislative Framework
MODEL ACT FOR THE TRANSPORT OF DANGEROUS GOODS BY ROAD AND RAIL 2007
MODEL SUBORDINATE LAW FOR THE TRANSPORT OF DANGEROUS GOODS BY ROAD AND RAIL
Australian Dangerous Goods Code (ADG7.7)
IMDG CODE (SEA TRANSPORT)
IATA REGULATIONS (AIR TRANSPORT)
Notes: 5
There are four key pieces of Legislation which cover the storage and handling and transport of dangerous goods.
These are ,
Storage and handling of dangerous goods
Australian code of transport of DG's by road and rail
IMDG code for transport by sea
IATA code for transport by air
There are others which we will discuss later

## Slide 6: LEGISLATIVE FRAMEWORK - VICTORIA
DANGEROUS GOODS ACT 1985
DANGEROUS GOODS (STORAGE AND HANDLING) REGULATIONS 2022
DANGEROUS GOODS (TRANSPORT BY ROAD OR RAIL) REGULATIONS 2018
Notes: 6
There are four key pieces of Legislation which cover the storage and handling and transport of dangerous goods.
These are ,
Storage and handling of dangerous goods
Australian code of transport of DG's by road and rail
IMDG code for transport by sea
IATA code for transport by air
There are others which we will discuss later

## Slide 7: Hazardous Substances
Hazardous Chemicals regulated in nationally harmonised Work Health & Safety (WHS) laws:
  ACT, NSW, NT, QLD, SA, TAS, WA, Commonwealth
  In VIC, Hazardous Substances are regulated under existing OHS laws:
  WA has adopted modified WHS laws, but Dangerous Goods remain outside
National review of WHS laws in 2019
GHS edition 7 mandatory as of 1-Jan-2023 after 2-year transition (replacing edition 3)

## Slide 8: Safe Work Australia
  Australian Government statutory body –
Responsibility for improving work health and safety and workers’ compensation arrangements across Australia
Safe Work Australia is not a regulator, no regulatory powers

## Slide 9: Transport of Dangerous Goods
Not covered by the Work Health & Safety (WHS) regulations for hazardous chemicals
These remain covered by transport laws and the Australian Dangerous Goods (ADG) Code, as implemented in each state.
  Administered by National Transport Commission (NTC)

## Slide 10: Hazardous Substances
Hazardous substances (VIC) are those that, following worker exposure, can have an adverse effect on health.
  Examples include poisons, substances that cause burns or skin and eye irritation, and substances that may cause cancer.
  Many hazardous substances are also classified as dangerous goods.
  In other states, WHS Regulations refer to Hazardous Chemicals instead of Hazardous Substances
Notes: 10

## Slide 11: Safety Data Sheet (SDS)
A Safety Data Sheet (SDS) is a technical bulletin containing detailed information about a hazardous substance.
  Formerly known as a Material Safety Data Sheet (MSDS)
An SDS must comply with VIC OHS Regulation 145
  WHS Regulations Part 7.1 Division 2
The hazard identification for the substance must be determined in accordance with the GHS.

## Slide 12: GHS
Globally Harmonised System of Classification and Labelling of Chemicals (GHS)
Internationally recognised system for the classification of chemicals
Developed by a United Nations (UN) committee

## Slide 13: Australian Dangerous Goods Code Edition 7.7 (ADG7.7)
ADG7 replaced ADG6 from 2007
  ADG7.7 adopted from 1 October 2020, mandatory from 1 October 2021
  Based on UN21
  ADG 7.8, based on UN22, adopted for use from 1 April 2023.
  Mandatory from 1 October 2023.

## Slide 14
To be able to identify and be aware of the hazards of Dangerous Goods
To make the Storage and Handling of Dangerous Goods safer
Objectives

## Slide 15: Changes in ADG7.5
New lithium battery mark
“Retail Distribution Load” replaced by “Concessional Limited Quantities”

## Slide 16: Changes in ADG7.6
  “Subsidiary Hazard” replaced the term Subsidiary Risk
  Minor classification changes
  New UN Numbers
  Inclusion of “Excepted Quantities” (column 7b) in Table 3.2.3 Dangerous Goods List

## Slide 17: Changes in ADG7.7
Simplified Limited Quantity requirements
Amended special provisions and packing instructions for automotive battery transport

## Slide 18: Changes in ADG7.8
Not as significant as previous versions
Updated table of exempted consignments to the UN Model Regulations and the ADG Code.
  Exempts very small quantities of DGs from the code’s provisions.
  Aligns with limited quantity concessions for dangerous goods and Lithium batteries.
Other provisions affecting containers and packaging.

## Slide 19: Dangerous Goods in the Workplace
Under VIC DG (Storage & Handling) Regulations
Equivalent obligations in:
  WHS Regulations (all states except VIC & WA): Schedule 11 hazardous chemicals
  WA Dangerous Goods Safety (Storage and Handling of Non-explosives) Regulations

## Slide 20: Duties of manufacturers and suppliers
Determine if goods are dangerous goods
Prepare SDS
Correctly package, mark and label the dangerous goods
Classify the dangerous goods
Provide SDS
Notes: 20

## Slide 21: Duties of Occupier (or PCBU)
Consultation
Induction & training
Obtain SDSs
DG Register
Safety signage / placarding
Packaging & marking
Hazard identification & risk control
Stability
Isolation / Segregation
Bunding
Transfer
Ignition sources
Security
Emergency planning / Incident response
Fire protection
Notes: 21

## Slide 22: Dangerous Goods Register
Required for all Dangerous Goods Locations
List of product names of all Hazardous Substances in the workplace, including Dangerous Goods and combustible liquids,
Accompanied by the current SDS
Can (should!) be combined with Hazardous Substance Register

## Slide 23: DG & Hazardous Substance Register
Supplier | Product | Issue Date | Expiry Date | Eye Hazard | Skin Hazard | Inhalation | Ingestion | DG Class
BOC Gases | Acetylene | 19/08/2021 | 19/08/2026 | No | No | No | No | 2.2 Non-Flammable Non-Toxic Gas
BOC Gases | Argoshield Light | 19/08/2021 | 19/08/2026 | No | No | No | No | 2.2 Non-Flammable Non-Toxic Gas
BOC Gases | Oxygen, Compressed | 19/08/2021 | 19/08/2026 | No | No | No | No | 2.2 Non-Flammable Non-Toxic Gas
bp | Automotive Diesel Fuel | 8/06/2019 | 7/06/2024 | Yes | Yes | Yes | Yes | No
bp | Regular Unleaded Petrol | 26/05/2021 | 26/05/2026 | Yes | Yes | Yes | Yes | 3 Flammable Liquid
Castrol | Activ 2T | 15/12/2022 | 15/12/2027 | No | No | No | No | Combustible Liquid
Castrol | GTX 20W-5 | 10/03/2023 | 9/03/2028 | No | No | No | No | No
Cement Australia | Blended Cement | 24/03/2023 | 23/03/2028 | No | No | No | No | No

## Slide 24: Threshold Quantities (Victoria)
Three thresholds are defined in the Dangerous Goods (Storage and Handling) Regulations
  Placarding Quantity
  Manifest Quantity
  Fire Protection Quantity
The quantities are given in Schedule 2 of the Regulations

## Slide 25: Schedule 2 (extract)

## Slide 26: Threshold Quantities – WHS States
Categories based on GHS physical hazards, largely aligned with DG classes
Thresholds are slightly different
  Placarding Quantity
  Manifest Quantity
  There is no Fire Protection Quantity
The quantities are given in Schedule 11 of the WHS Regulations

## Slide 27: WHS Regs Schedule 11 (extract)
Source: Commonwealth Work Health and Safety Regulations 2011, Schedule 11

## Slide 28: Threshold Quantities – WA
Quantities are as per Dangerous Goods Safety (Storage and Handling of Non-explosives) Regulations, Schedule 1:
  Placarding Quantity
  Manifest Quantity
  10 x DG manifest quantity requires DFES Emergency Response Guide (except petrol stations and mine sites).
Continues under WA WHS legislation.

## Slide 29: Threshold Quantities – WA (Schedule 1)
Source: WA Dangerous Goods Safety (Storage and Handling of Non-explosives) Regulations 2007, Schedule 1 — Quantities of dangerous goods

## Slide 30: NZ HSW (HS) Regs
Schedule 4 Quantities of hazardous substances that require fire extinguishers
Schedule 5 Threshold quantities for emergency response plan

## Slide 31: Quantity Measurement Bulk
Non liquid – the mass (kgs) the container is designed to hold
Liquid – the design capacity of the container in litres
  In example: 30,000 litres
Gas – total capacity of the container
Solids not in container – undivided mass in kgs
30,000 LITRES
10,000 LITRES

## Slide 32: Quantity Measurement Packaged
Non liquid – net mass (kgs) in container
Liquid – net capacity of the container
Gas – Total capacity of the container

## Slide 33: Quantity Measurement - Articles
The net quantity of that part of the article that is Dangerous Goods
12 x 350 g = 4,200 g = 4.2 Kg

## Slide 34: Minor Storage
Quantities less than the placarding quantity
  Note: There may be several minor quantity stores on a site.
Ensure containers are properly labelled
Maintain Register and SDSs
Provide suitable PPE
Ensure adequate segregation
Ensure suitable spill management
Provide training
Provide security
Manage waste disposal

## Slide 35: Placard Quantities
Placard site and storage facilities
Identify hazards
Perform risk assessment
Take risk control measures
  Storage and handling
  Transfer
  Segregation
  Ignition sources
  Spill control
  Ventilation

## Slide 36: Manifest Quantity
Notification to workplace safety regulator
  VIC requires 2-yearly update to WorkSafe (changed from 5-yearly on 1 July 2021)
  Licence required in SA, WA
  See regulator websites in other States
Prepare Manifest
  Shows location of storage facilities and quantities in each store
Prepare written Emergency Plan
  (Approved by Fire Authority – VIC)

## Slide 37: Dangerous Goods Manifest
9. DRUM STORAGE
CLASS 3 10,000 L CLASS 8 6,000 L
CAR PARKING
TRUCK ENTRANCE
TRUCK EXIT
TRIPLE INTERCEPTOR
TANK | PRODUCT | VOL. (L) | DG CLASS
1 | MEK | 10,000 | 3, PG II
2 | WHITE SPIRIT | 20,000 | 3, PG III
3 | WASTE OIL | 20,000 | C2
4 | HEATING OIL | 30,000 | C1
5 | BASE OIL 150 | 55,000 | C2
6 | BASE OIL 460 | 55,000 | C2`
8 | CAUSTIC SODA | 5,000 | 8, PG II
XYZ CHEMICALS
WAREHOUSE
LABORATORY
BLEND TANKS
4
3
2
1
5
6
8
BT6
BT5
BT4
WORK-SHOP
7. Gas bottle Storage
FILLING LINE
WASTE STORAGE
GAS METER
OFFICES
BT1
BT2
BT3
DRUM
STATION
FIRE
HYDRANT
EMPTY DRUMS

## Slide 38: Fire Protection Quantity (VIC only)
Obtain written report from Fire Brigade re adequacy of fire protection services

## Slide 39: DFES Emergency Response Guides (FES-ERGs – WA only)
Required at sites that store or handle more than 10 x manifest quantity (except petrol stations and mine sites).
Designed to provide essential information to the Department of Fire and Emergency Services (DFES) for use in an emergency at larger dangerous goods sites.

## Slide 40: Segregation
Segregation of chemicals in a warehouse, is of critical importance to the manager and the operator.
Principally achieved by Class
Sub-hazards must also be considered when determining segregation
Notes: 40
MAKE SPECIAL MENTION OF -
AUSTRALIAN STANDARDS FOR STORAGE AND HANDLING OF CLASS EIGHT (CORROSIVES)
SUB-hazardS MUST BE TAKEN INTO CONSIDERATION.
GAS CYLINDERS SHOULD BE STORED OUTSIDE.
4.3 DANGEROUS WHEN WET MUST BE STORED IN A DRY STORE. IE NO SPRINKLERS.
POWDERS WITH AN EXPLOSION HAZARD TO BE STORED NEAR THE FLOOR.

## Slide 41
Some interactions can be violent.
Nitric Acid (Class 8 - Corrosive/Class 5.1 Oxidising Agent) + Ethanol (Class 3 - Flammable Liquid)
will lead to an explosion with the liberation of fumes of nitrous oxide, acetaldehyde and formaldehyde.
Some interactions can liberate very poisonous gases.
Hydrochloric Acid (Class 8 - Corrosive) +
Sodium Cyanide (Class 6.1 - Poison)
will liberate extremely poisonous Hydrogen Cyanide.
Some interactions can liberate heat and acid fumes.
Sulphuric Acid (Class 8 - Corrosive ) +
Sodium Hydroxide (Class 8 - Corrosive)
will liberate much heat and fumes.
Notes: 41

## Slide 42: Segregation
Flammables
Corrosives – Acids
Oxidisers
Corrosives – Alkalis
Notes: 42

## Slide 43: Segregation
See Appendix 2 of the Code of practice for the storage and handling of dangerous goods (VIC)
Notes: 43

## Slide 44: Bunding – Package Storage
The capacity of the spillage containment compound shall be at least 100% of the volume of the largest package, plus 25% of the storage capacity up to 10 000 L, together with 10% of the storage capacity between 10 000 L and 100 000 L, and 5% above 100 000 L.
  Source: AS 1940:2017, part 4.4.3(d) Spillage containment
NOTE: Allowance must also be made for fire and storm water if appropriate
Notes: 44

## Slide 45: Bunding – Bulk Storage
Notes: 45

## Slide 46: Other matters to consider
Transit storage
Site plan
Hazmat box and its location

## Slide 47: Placarding for Storage
There are four ‘types’ of placard under the Dangerous Good Regulations – these are:
  Outer warning placards
  Information placards for stated Dangerous Goods in tanks
  Information placards for stated Dangerous Goods in Packages; and
  Information placards for stated combustible liquids in tanks or packages

## Slide 48: Outer Warning Placard
HAZCHEM
600 mm
120 mm
100 mm Lettering
Notes: 48

## Slide 49: Package Store Placard
100 mm
Notes: 49

## Slide 50: Bulk Tank Placard
AMMONIA,
ANHYDROUS
HAZCHEM
2RE
UN No.
1005
100 mm
100 mm
50 mm
50 mm
200 mm
150 mm
800 mm
400 mm
Notes: 50

## Slide 51: Combustible Liquid Placard (GHS: Flammable Liquid Category 4)
Placard quantity is 10,000 litres
Applies to diesel fuel storage (above-ground only)
COMBUSTIBLE LIQUID
100 mm Lettering
Notes: 51

## Slide 52: New Zealand Signage Format
HAZCHEM
COMBUSTIBLE LIQUID
KEEP AWAY FROM IGNITION
SOURCES – NO SMOKING
TOXIC TO AQUATIC LIFE
CONTAIN SPILLS, PROTECT WATERWAYS
IN CASE OF FIRE
CALL 111 – ASK
FOR FIRE
DEPARTMENT
IN CASE OF
SPILL CALL
AUCKLAND
CITY COUNCIL
POLLUTION
HOTLINE
09 377 3107
>10,000L BULK DIESEL
HAZCHEM
TOXIC TO AQUATIC LIFE
CONTAIN SPILLS, PROTECT WATERWAYS
IN EMERGENCY DIAL 111, FIRE, POLICE OR AMBULANCE
For urgent medical advice: National Poisons Centre Dial 0800 POISON (0800 764 766)
1,000L - <10,000L BULK DIESEL

## Slide 53: Segregation Exercise

## Slide 55: Road and Rail Transport
Packaging
Placard loads
EIPs
Limited and Excepted Quantities
Shipping documentation
Bulk transfer

## Slide 56: ADG uses container based approach
Large packagings
  Capacity ≤3 m3, containing
    articles or inner packaging with net mass >400 kg, or
    total capacities >450 L
Bulk containers (solids, >1 m3 capacity)
Portable tanks (>450 L)
IBCs (Intermediate Bulk Containers, ≤3,000 L)
Tank vehicles
Multiple element gas containers (MEGCs)
Gas cylinders
Pressure drums

## Slide 57: MEGCs

## Slide 58: Aggregate Quantity
The total of
  the number of kilograms of:
    solid dangerous goods; and
    articles (including aerosols); and
  the number of litres or kilograms, whichever is used in the transport documentation to describe the goods, of liquid dangerous goods; and
  the total capacity in litres of receptacles containing dangerous goods of Class 2 (except aerosols).

## Slide 59: Limited & Excepted Quantities
  The ADG has adopted rules for transport of Dangerous Goods in limited quantities without vehicle placarding, licensing and other controls
  Chapter 3.4: “the transport of certain small quantities of dangerous goods may be conditionally exempt from the Regulations and this Code”.
  Chapter 3.5 “Excepted quantities of dangerous goods of certain classes, other than articles, meeting the provisions of this Chapter are not subject to any other provisions of this Code”.
  Specific provisions apply to inner, intermediate and outer packaging, and to segregation

## Slide 60: Limited & Excepted Quantities
  Limited Quantities are listed in Column 7a of Table 3.2.3
  Excepted quantities are in Table 3.2.3 column 7b
Limited Quantity mark
Excepted Quantity mark
100 mm

## Slide 61: Limited & Excepted Quantities

## Slide 62: Limited & Excepted Quantities & Concessional Limited Quantities
In 2017 ADG7.5 replaced Retail Distribution Loads with Concessional Limited Quantities (CLQ), including domestic consumables dangerous goods, requirements.
In 2018 ADG7.6 introduced Mixed Packet (Lower Risk) Dangerous Goods provisions, and Personal Care Products in consumer packaging provisions.

## Slide 63: ADG7.7 simplifies Limited Quantity requirements further
LQ sub-categories removed:
  Concessional Limited Quantity
  Mixed Packet (Lower Risk) Dangerous Goods
  Personal Care Products in Consumer Packaging.
DG Transport Documentation no longer required
  Documentation to state load “Contains Dangerous Goods Packed in Limited Quantities”.
Placarding requirements also change.

## Slide 64: Domestic Consumable DGs
LQ segregation, overpack and documentation concessions extend to Domestic Consumable DGs that are packed and intended for retail distribution, which are defined as including:
  party poppers;
  sparklers and bon-bons (UN0337),
  domestic smoke detectors (UN 2911),
  lighters and lighter refills (UN1057) or
  portable fire extinguishers with compressed or liquefied gas up to 23kg gross weight (UN 1044).
See LQ guidance document in webinar attachments.

## Slide 65: Placard load – LQ or DC
A load that contains Limited quantity and / or domestic consumable DGs that :
  Includes aggregate quantity of any 1 UN number from a single place of consignment:
     2,000 L or Kg
  Does not include aggregate quantity of any 1 UN number from a single place of consignment:
     8,000 L or Kg
  See ADG 7.7 Table 5.3.2
If consigning a mixed load of LQ/DC and fully regulated DC, see ADG 7.7 Table 5.3, NOTE 5, or p. 14-15 of NTC Guidance document, Consigning and transporting dangerous goods packed in limited quantities.

## Slide 66: Overpacks
An enclosure containing one or more Dangerous Goods packages – e.g.:
  pallet secured by shrink wrapping or similar,
  protective outer packaging such as a crate.
The word “OVERPACK” should be displayed in lettering at least 12 mm high.
  NOT required if the overpack is intended only for transport by road or rail within Australia.

## Slide 67: Overpacks
Packages in an overpack must be secured to minimise damage during transport.
Incompatible dangerous goods must not be transported together in an overpack, unless limited quantity provisions are met.
Overpack must be labelled with proper shipping name, UN number and marks for all DGs,
  OR
With the Limited Quantity mark.

## Slide 68: Overpacks

## Slide 69: Intermediate packaging
Compulsory for limited quantities …
  … of class 8, PGII in glass, porcelain or stoneware
  … in inner packagings that are liable to break or be easily punctured, e.g. glass, porcelain, stoneware or certain plastics.
    ADG7.7 clause 3.4.2.3
Absorbent material required for liquids

## Slide 70: Intermediate packaging

## Slide 71: Segregation in Placarded Loads

## Slide 72: Licencing
A DG driver’s licence AND a DG vehicle licence are required to transport DGs:
  In a receptacle with capacity > 500 L or KG
  A licence is not required to transport DGs in IBCs with a total capacity > 3,000 L that are not packed or unpacked on the vehicle.

## Slide 73: Placard load (other than LQ/DC)
Dangerous goods in a receptacle with a capacity of >500 L or Kg, OR | Aggregate quantity of DGs of ≥250 L or Kg that includes — Division 2.1 Flammable Gases (except aerosols), OR Division 2.3 Toxic Gases; OR Dangerous goods in any class of Packing Group I, OR
Division 6.2 Class A – all quantities Other classes – ≥ 10 KG/L, OR | Aggregate quantity of DGs (other than LQ) of ≥1,000 L or Kg

## Slide 74: Placarding of Package Vehicles
A vehicle carrying a Placard Load must be placarded with:
  If one Class:
    A Class Label (and sub-hazard if applicable) at the FRONT & REAR
  If more than one Class:
    Mixed Class Label
      OR
    all Individual Class Labels
Non-placard loads may be placarded

## Slide 75: Vehicle Placarding – Packaged DGs
RIGID TRUCK
SEMI-TRAILER
TRUCK-TRAILER
B-DOUBLE

## Slide 76: Placarding of Bulk Vehicles
Rule 1:
  All vehicles carrying Bulk Dangerous Goods must be placarded
Rule 2:
  The placards must be clearly visible at all times during transport

## Slide 77: Placarded Bulk Vehicles
Bulk Dangerous Goods
Front of the vehicle
  Class label (and sub-hazard if applicable)
  If more than one class,
    The mixed Class Label, or
    Individual Class Labels
Both sides and the rear
  Emergency information panels - either;
    Individual EIP
    Mixed load (refined petroleum product) EIP, or
    Multi-load EIP

## Slide 78: Vehicle Placarding Bulk DGs (including IBCs)
RIGID TRUCK
SEMI-TRAILER
TRUCK-TRAILER
B-DOUBLE

## Slide 79: Emergency Information Panel (EIP)
PETROL
HAZCHEM
3YE
UN No.
1203
100 mm
100 mm
600 mm
IN EMERGENCY, DIAL
000, POLICE OR FIRE BRIGADE
SPECIALIST ADVICE
XYZ FUEL COMPANY 1800-005-411
800 mm
250 mm
100 mm
Notes: 79

## Slide 80: Emergency Information Panel (EIP)
NITRIC ACID,
RED FUMING
HAZCHEM
2PE
UN No.
2032
200 mm
150 mm
IN EMERGENCY, DIAL
000, POLICE OR FIRE BRIGADE
SPECIALIST ADVICE
ABC CHEMICAL COMPANY 1800-116-522
50 mm
50 mm
Notes: 80

## Slide 81: Placarding Mixed Load Vehicles
Dangerous Goods in both Bulk and Packages aboard same vehicle
Same Class
  Mark as for bulk of that Class
Different Classes
  Front and rear – mixed Class Label
  Both sides and rear
    Emergency information panels appropriate to the bulk Dangerous Goods aboard

## Slide 82: Use of Multi-Load EIPs
Where a multi-compartment tanker contains Dangerous Goods that are not the same –
  All EIPs to be Multi-load
Where a vehicle carries portable bulk containers holding different Dangerous Goods –
  Enclosed vehicle – All Panels Multi-load
  Open vehicle – Rear panel Multi-load (provided EIPs on containers visible from sides)

## Slide 83: Mixed Load EIP
HAZCHEM
3YE
UN No.
MULTI-LOAD
IN EMERGENCY, DIAL
000, POLICE OR FIRE BRIGADE
SPECIALIST ADVICE
XYZ FUEL COMPANY 1800-005-411
250 mm
Notes: 83

## Slide 84: Placements of EIPs
Side Panels
On a vehicle (includes tankers):
  As close as possible to the front
On a Bulk Container or Freight Container:
  Any position
Rear Panel
  Any position as long as clearly visible
  All EIPs must be in a substantially vertical plane
  Lower edge at least 450mm above the ground

## Slide 85: EIPs on Bulk Containers
IBCs may have smaller Emergency Information Panels
  i.e. 400mm x 300mm
If EIPs attached to a Bulk Container are visible from both sides – no further EIPs needed on the sides of the truck or trailer
Fully complying EIP, i.e. 800 mm x 600 mm is required on the rear

## Slide 86: Placarding Bulk Containers
Must be placarded on each side with an emergency information panel (EIP)
An EIP must also be visible from the rear
Notes: 86

## Slide 87: Placarding Freight Containers carrying a Placard Load
Packaged Dangerous Goods
Same Class and UN No
  Class and sub-hazard (if applicable) & UN No
Same Class but different UN Nos
  Class and sub-hazard (if applicable)
Different Classes
  Either or both of –
    Mixed Class labels
    Class labels for each of the Dangerous Goods
Bulk Dangerous Goods
  Emergency information panels

## Slide 88: Removal of EIPs
EIPs must be removed from containers which have been purged
Rear EIP on a bitumen spray vehicle may be removed during spraying operations

## Slide 89: Container Placarding for transport by sea and air
This type of labelling is required for transport by sea (IMDG Code) and air (IATA / ICAO).
It DOES NOT apply to consignments of dangerous goods being transported only by road or rail within Australia.
Intermodal containers can be transported to and from ports if they have been placarded in accordance with IMDG or IATA Regulations.
See ADG 7.7 part 5.3.2.1.

## Slide 90: NZ Road Transport Placards
Loaders and drivers must placard vehicles and freight containers … whenever the load is over 50 kilograms or 50 litres.
The only exception to this is if the load is dangerous goods in excepted quantities or excepted packages of radioactive material, transported in accordance with clause 2.9 of the rule.
Examples of dangerous goods placards:
Source: https://nzta.govt.nz/driver-licences/getting-a-licence/licences-by-vehicle-type/transporting-dangerous-or-hazardous-goods/dangerous-goods-carried-by-transport-operators/

## Slide 91
Vehicle Placarding Exercise

## Slide 92: Container Placarding for transport by sea and air
European and some South American intermodal bulk containers may display a Hazard identification number in the top half of an orange panel, with the 4-digit UN number in the bottom half.
The first digit indicates the primary hazard, the second and third digit generally indicate secondary hazards.
  Doubling of a digit indicates an intensification of that particular hazard (i.e. 33, 66, 88)
  Where the hazard associated with a substance can be adequately indicated by a single figure, this is followed by a zero. (i.e., 30, 40, 50)
  • A hazard identification number prefixed by the letter 'X', indicates that the substance will react dangerously with water. (i.e., X88)

## Slide 93: Shipping Documentation
Required for all DG loads except LQ / DC
Must be:
  In English
  In hard copy
  Carried in an emergency information container

## Slide 94: Shipping Documentation (Cont…)
DG and non-DG may be entered on the same document; however, DG must be entered first
On a multi-trailer vehicle (e.g. B-Double), documents should indicate which goods are stored on each unit
Tankers should carry a run-sheet indicating approximately how much product is remaining

## Slide 95: Shipping Documentation (Cont…)
Documentation is made up of two parts
  Product Information
  Emergency Information

## Slide 96: Product Information
Proper shipping name
Class and Sub-hazard (if applicable)
UN No.
Packing Group
Total quantity
For Bulk: (Portable)
    Description of each type of container e.g. ‘IBC’ and number of containers
For Packages:
    Description of each type of package e.g. ‘drum’ and number of packages

## Slide 97: Example transport document

## Slide 98: Emergency Information
Approved types include:
  Dangerous Goods – Initial Emergency Response Guide (HB 76:2010, SAI Global)
  Australian & New Zealand Emergency Response Guide Book 2021
    Replaces Australian Emergency Response Guidebook 2018
Australian emergency contact information MUST be included

## Slide 99: Dangerous Goods – Initial Emergency Response Guide

## Slide 100: Australian & New Zealand Emergency Response Guide Book 2021

## Slide 101: Transfer of Bulk Dangerous Goods
Positioning vehicles for transfer
Control of ignition sources during transfer of flammables
Bonding
Filling levels
Prevention of movement during transfer
Person to remain at vehicle
No person in cabin
Notes: 101

## Slide 102: Transfer of Bulk Dangerous Goods
Is the Responsibility of the Transferor –
who is usually the Driver
  Now includes transfer of bulk solids
Notes: 102

## Slide 103: Ullage Space in Container
Any transport tank containing liquid either:
  Single compartment of more than 8600 litres or
  Multiple compartments any one of which exceeds 8600 litres
Must not be driven with an ullage space of between 20% and 85%
This rule does not apply to Class 2 Dangerous Goods or Cutback Bitumens
Notes: 103

## Slide 104: Ullage Space in Container
Source: https://www.linkedin.com/posts/alex-gover-3a2a87139_a-unique-look-at-the-fluid-dynamics-in-a-ugcPost-6565175346348474368-JBb4

## Slide 105: Positioning of Vehicle
Two options:
Position so it can be driven away in a forward direction –
  or, if not possible,
so it can be driven away with minimal manoeuvring
Notes: 105

## Slide 106: Before Transfer
Ensure
  There is sufficient space in the tank to take what is being delivered
  Transfer hose is connected to the correct fill point
Notes: 106

## Slide 107: Hoses
No hoses to be run across areas accessible to vehicles, unless access is stopped.
Notes: 107

## Slide 108: Ignition Sources
No smoking or carrying of matches or lighters, on vehicles carrying Dangerous Goods of Classes (or with sub-hazards) of 2.1, 3, 4 or 5 in bulk
Notes: 108

## Slide 109: Ignition Sources during Transfer
Every hose connection point must be separated from ignition sources by not less than:
  10 metres for Class 2.1
  15 metres for Class 3, being filled into a tanker
  8 metres for Class 3, being discharged from a tanker
  8 metres for Class 4 or 5
Notes: 109

## Slide 110: Electrical Bonding – Class 3
Receiving tank to be electrically bonded to discharging tanker
Bonding lead to be connected when tank being filled or emptied
Exception – underground tanks
Notes: 110

## Slide 111: Vehicle Engines
For Class (or sub-hazard) 2.1, 3 or 4, the vehicle engine must be stopped before hose connections are made.
For all Dangerous Goods, the engine must remain stopped during discharge …
  … UNLESS required for pumping.
Notes: 111

## Slide 112: During Transfer
No person in the cabin
Person must remain at the vehicle, where the operation can be observed and all valves and equipment can be operated.
Notes: 112

## Slide 113: After Transfer
Make sure all valves have been closed and closures replaced
Walk around vehicle
Notes: 113

## Slide 114: URL - additional information
Australian Dangerous Goods Code (ADG )
  http://www.ntc.gov.au/heavy-vehicles/safety/australian-dangerous-goods-code/
Safe Work Australia
  www.safeworkaustralia.gov.au
National Transport Commission – ADG Code
  https://www.ntc.gov.au/codes-and-guidelines/australian-dangerous-goods-code
UN Model Regulations for the Transport of Dangerous Goods
  https://unece.org/info/publications/pub/364867
Global Harmonisation System (GHS) – UNECE
  https://www.unece.org/trans/danger/publi/ghs/ghs_welcome_e.html
Labelling of Agricultural and Veterinary chemicals
  https://apvma.gov.au/registrations-and-permits/labelling-codes
Poisons Schedule (SUSMP)
  https://www.tga.gov.au/publication/poisons-standard-susmp
Notes: 114

## Slide 115: URL - additional information
EPA NZ – Hazardous substances classification
  https://www.epa.govt.nz/industry-areas/hazardous-substances/new-zealands-new-hazard-classification-system/
WorkSafe New Zealand – Hazardous Substances
  https://www.worksafe.govt.nz/topic-and-industry/hazardous-substances/
Hazardous Substances Toolbox
  https://www.hazardoussubstances.govt.nz/
NZ Land Transport Agency
  https://nzta.govt.nz/resources/rules/dangerous-goods-2005-index/
NZ Health and Safety at Work (Hazardous Substances) Regulations
  https://www.legislation.govt.nz/
Notes: 115

## Slide 116: Australian & New Zealand Standards
  AS 1940–2017 The storage and handling of flammable and combustible liquids
  AS 2243.2:2021 Safety in laboratories, Part 2: Chemical aspects and storage
  AS 3780–2008 The storage and handling of corrosive substances
  AS/NZS 3833:2007 The storage and handling of mixed classes of dangerous goods, in packages and intermediate bulk containers
  AS 4332–2004 (R2016) The storage and handling of gases in cylinders
  AS/NZS 4452:1997 The storage and handling of toxic substances
  AS/NZS 4681:2000 The storage and handling of Class 9 (miscellaneous) dangerous goods and articles
  AS/NZS 5026:2012 The storage and handling of Class 4 dangerous goods
  NZS 5433:2020 Transport of dangerous goods on land
  SNZ HB 5433:2021 UN dangerous goods list

## Slide 117: Sources of information
Physical inspection
Internal and external audits
Employee knowledge and expertise
Trade journals
WorkSafe alerts and publications
Incident /injury records
Industry associations
Notes: 117

## Slide 118: Sources of information
Product information
Technical data sheets
Manufacturers instruction manuals
Personal contacts
By asking ‘What if ?’
Brainstorming
Notes: 118

## Slide 119: AEBN SERIES 2: Dangerous Goods and Hazardous Substances Workshop Webinar 5 April 2023 Presented by Australian Environment Business Network (AEBN) National Office 100 Douglas Pde Williamstown Vic 3016 (PO Box 588 Altona Vic 3018) T +61 3 9397 2511 | E aebn@aebn.com.au www.aebn.com.au